## Slide 1
GAUSSIAN SPLATTING
From rover photos
to a walkable
piece of Mars
241 Perseverance photos of Cheyava Falls became 972,047 Gaussians, in real metres, without ever guessing where a camera was.
Planetary Scene Studio · MHacks
Right: our splat in the viewer, from rover height.

## Slide 2
STEP 1
Start from real photos, from three parking spots
A splat needs the same ground seen from different places. One stop only gives rotation; three give depth.
Planetary Scene Studio · how the Mars splat was made
Mastcam-Z: a rock and the rover's wheel tracks
Mastcam-Z: where the sample was drilled
Where the rover stood, to scale
241 photos from NASA's public Mars 2020 feed, sols 1195 to 1210
2 cameras Navcam (wide stereo pair) and Mastcam-Z (zoom, colour)

## Slide 3
STEP 2
Get the geometry from NASA, not from guesswork
Every image ships with its camera model and the rover's position, so the scene is in metres from the first step. No structure-from-motion.
Planetary Scene Studio · how the Mars splat was made
Fisheye Navcam frame, straightened with its JPL camera model
Depth from the two Navcam eyes, 42 cm apart (red is near)
One spot (red circle) located in photos from other stops, from rover telemetry alone
0.1 px stereo matching error after undistorting, down from about 1 px
312,136 3D points from stereo, used as the starting positions
2 px worst misalignment between the three stops after registration (our limit: 3)

## Slide 4
STEP 3
Train, then judge by looking
gsplat with the MCMC strategy on a Colab A100. The usual score barely moved between good and bad runs, so every run was rendered from new viewpoints.
Planetary Scene Studio · how the Mars splat was made
First run: fine from the training cameras, spikes from anywhere else
Final run, same viewpoint
30,000
steps
25 min
on one A100
2.5 M
Gaussians
Fix 1 a depth-loss bug that produced NaNs
Fix 2 two regularisers that removed Gaussians seen by only a few photos
Fix 3 a penalty on needle-shaped Gaussians, which were the spikes

## Slide 5
STEP 4
Put it on the map, and make it data
Cropped to the 9 m that the photos cover well, placed on NASA's orbital terrain in the same metric frame, with a layer value on every Gaussian.
Planetary Scene Studio · how the Mars splat was made
The same 18 m disc: 38 x 36 orbital pixels on the left, our splat on the right
972,047
Gaussians in a 16 MB file
270
orbital height samples in the same disc
Layers
terrain class, roughness, search cluster on every Gaussian
10 cm
surface map the rover drives on
Limits: soft from closer than about 2 m, and holes where no photo covers the ground.